## Slide 1: Augmented Reality Cornell Cup Mid Review Fall 2012
Stephen Carlson
Stephen Ellis
Thor Smith
Thor
Smith
Steven
Ellis
Stephen
Carlson

## Slide 2: Outline
Challenge Definition
Project Entry Solution
Accomplishments to Date
Technical Ingenuity
Project Execution Overview
Complications
Opportunities
Recommendations and Next Steps

## Slide 3: Challenge Definition
Wearable computing is emerging quickly
  Google Glass, Samsung Galaxy Gear, and Oculus Rift.
Combine virtual reality with reality to create augmented reality
  Provide information
  Promote Teamwork
  Decrease need for physical objects
The design will need to satisfy the following requirements:
  Portable and Comfortable
  Track user position and head orientation
  Wireless Communication
  Easy to set up and use
  Transparent display, easy to see

## Slide 4: USE cases
Artistic Performance
  Performers need to know where to be and when.
Train a New Employee
  Show a physical demonstration of equipment
  Employee may observe machinery in operation.
Children Playing Games
  Children Rely on “imaginary” objects placed in a select location.
Educational Demonstrations
  Replace resources with virtual resources placed in appropriate locations.

## Slide 5: Project entry solution
Will not focus on internet connectivity
Allow for multiple simulations.
Focus on Gaming
Headset:
  Provide the display
  Mounting point for sensors
Backpack:
  Wireless communication
  Graphics rendering
  Simulation Logic

## Slide 7: Accomplishments To Date
PHASE 1
PHASE 2

## Slide 8: Accomplishments To Date (PHA1)
Hardware
  Interfacing to Inertial Measurement Unit
  Interfacing to GPS
  Power management
    Battery charging
    Battery fuel gauge
    Voltage regulation

## Slide 9: Accomplishments To Date (PHA1)
Self-contained headset
  Hard hat with display and all
  electronics mounted to rails
Software
  OpenGL ES for 3D rendering
  Networking: XBees with CCU
  SPI communication between Pi and micro
  MacPan game

## Slide 10: Hardware metrics
Metric | Target | Description
Mass | Headset: 1 kg Backpack: 3 kg | Neither the headset nor the backpack can be too heavy to impede the performance of typical activities by the user.
Power | 3 hours runtime | Augmented reality applications run for long durations, so the device must operate long enough on battery power to be usable. The remaining battery capacity should be displayed to the user.
Location | Minimum 2 meter accuracy and precision | The accuracy of the rendered virtual world depends heavily on the accuracy and precision of the user’s geospatial position.
Wireless | 80 m range, line of sight | A unique feature of this device is the wireless coordination capability of multiple headsets in the same virtual environment. The current wireless signal strength should be reported to the user.
Comfort | No running speed or vision reduction | Ideally, the user would be able to perform actions without a noticeable burden on the user. It is difficult to quantitatively measure comfort, but the user should be able to orient their head, see the environment, and move from place to place as effectively as if the device was not worn.
Durability | Operate from 0 to 40 C indoors and outdoors in dry conditions | Most augmented reality applications involve users walking or running, which will subject the device to vibration and light impacts. In addition, sunlight, humidity, and dust are inherent concerns for a portable device.
Usability | End user can start up and use device without a technician | A user unfamiliar with the device technical details must be able to power on the device, perform start-up procedures such as wireless connection, and load the desired application.

## Slide 11: Software metrics
Metric | Target | Description
3D Graphics | Minimum 5000 polygon count | The user will expect to see a good 3d image. Phase 2 offers opportunities to increase graphical performance.
Graphics | Minimum 20 Hz update rate | We will need to render ghosts and the maze walls in real time according to the user’s geospatial location and their head orientation.
Collision Detection | Minimum 2 meter accuracy and precision | The ability of the software to detect collision detection will be affected by the accuracy of the GPS. The minimum required to be meaningful cannot exceed a couple of meters. This means ghosts could be 2 m2 to account for accuracy of GPS.
Network User Position Update Rate | Minimum of 20Hz (50ms). | The position and orientation of each headset will need to be communicated wirelessly at least every 50ms to keep up with the GPS and provide meaningful feedback about collisions to each headset.
Network Graphic Position Update Rate | Minimum of 20Hz (50ms) | The position information about positions of ghosts and other virtual objects needs to be updated in a timely manner and should at least be as fast as the update rate of the player’s position.
User Interface Usability | End user can navigate the user interface intuitively. | A user unfamiliar with the operation of the software should be able to figure it out with minimal references to the user manual. For phase 1 this will be displayed from the control unit. In phase 2 the user interface will migrate to the headset’s display.

## Slide 12: Accomplishments To Date (PHA2)
Power consumption testing
  Provided Terasic board uses 1.2 A typical (14.4 W)
  Acceptable battery life with 60 Whr capacity
Hardware design for Phase 2
  Power supply design
    Battery and regulator selection
  Headset interfacing board
    Re-use GPS, inertial measurement unit, microcontroller
Packaging
  Re-use optics
  Selected new display
  Selected helmet and backpack
[POWER CONSUMPTION]
[PCB]

## Slide 13: Technical Ingenuity
Display virtual environment overlay on real world
  Preserves real-world depth perception
  Large field of view
  Both worlds perceptible simultaneously
User head and position tracking
  Filtering algorithm for inertial measurement data
Portability and battery operation
Wireless communication to other headsets
  Multi-user augmented reality

## Slide 14: Execution overview – Timeline 1/3

## Slide 15: Execution overview – Timeline 2/3

## Slide 16: Execution Overview – Timeline 3/3

## Slide 17: Execution overview - BUDGET
Name | Item | Vendor | Unit Price | Shipping | Quantity | Price
Battery |  | BatterySpace | 66.95 |  | 2 | 133.9
Screen1 |  | AdaFruit | 139.95 |  | 1 | 139.95
Screen2 |  | AdaFruit | 64.95 |  | 1 | 64.95
IMU |  | Mouser | $28.75 |  | 1 | 28.75
GPS |  | SparkFun | 49.99 |  | 1 | 49.99
Passives |  | Various | 10 |  | 2 | 20
PCB |  | Oshpark | 40 |  | 2 | 80
Microcontroller |  | DigiKey | 11.45 |  | 2 | 22.9
Charger |  | BatterySpace | 39.95 |  | 2 | 79.9
Regulator |  | Mouser | 13.23 |  | 2 | 26.46
Fuel Guage |  | DigiKey | 6.43 |  | 2 | 12.86
3D printed Box |  | Purdue IEEE | 40 |  | 2 | 80
Backpack | Draw String Backpack | Supplied | 10 |  | 0 | 0
Total |  |  | 521.65 |  |  | 739.66

## Slide 18: COMPLICATIONS
Patent Liability
  Novelty of design avoids many AR patents
    Large fraction specifically mention cameras
  Licensing may be required
  Could file new patents and cross-license
User Safety
  LiFePO4 much safer than other Lithium battery chemistries
  Translucent display keeps user aware of environment
  Product unsuitable for use while driving, operating heavy machinery

## Slide 19: Opportunities
Selling software to users after purchase of device
  Need to set up distribution network
  Encourage third party development
  Anti-piracy solutions

## Slide 20: Recommendations and Next Steps
Continued software development
  Improve calculation of head orientation
  Improve filtering of GPS data
Migrate software to new motherboard
Finalize packaging modifications for larger display
Testing of new hardware
  Battery power and charging
  Interfacing of Terasic board with existing microcontroller
  Display

## Slide 21: Questions / Discussion

## Slide 22: PCB

## Slide 23: Schematic