## Slide 1: PCB Layout Narrative
Team 05 Augmented Reality Project
TCSP #05
Stephen Carlson, Steven Ellis, Alec Stephen Green, Thor Smith

## Slide 2: Abstract
We propose an augmented reality simulator
  Allows at least one user to play an electronic game in a mobile, outdoor environment
  Intended for gaming and other simulations that require an augmented environment
Contains two primary parts: a headset and a central control unit (CCU)
  The headset is worn by the user and overlays images of game objects on the user’s view of the environment
  The CCU remains stationary and communicates information to the headset about simulation logic.

## Slide 3: Functional Block Diagram
* CCU will not have a PCB

## Slide 4: PSSC Review
An ability to render graphics based on the orientation of the user’s head.
An ability to render graphics based on the user’s current geospatial location.
An ability to monitor and display the battery power level of the headset to the user.
An ability to monitor and display the status and quality of the wireless connection to the central control unit.
An ability to load headset graphics for a new simulation without re-flashing software on the headset’s microcontroller.

## Slide 5: Layout Considerations – General
Advanced Circuits/4PCB specs
  5mil trace/5mil space
  10mil minimum hole size and 5mil tolerance
For manufacturability
  10mil trace/8mil space
  15mil minimum hole size
No acute angles
Two layers

## Slide 6: Layout Considerations – MCU
Oscillator and USB lines match impedance
  Trace lengths must match
  No right angles
Decoupling, oscillator must be adjacent
  Place some capacitors underneath chip
Pin locations determine routing success

## Slide 7: Layout Considerations – Power
Total current could be up to 2A
  Use low resistance copper pours
  Multiple large vias for transfer between layers
  Power from multiple directions (“islands”)
  Bulk capacitors near regulator, bypass near loads

## Slide 8: Layout Considerations – Other
Connectors
  Raspberry PI connector must match motherboard
  Other connectors must be on edges
Route I2C, UART, SPI lines together
  Test points
Debug LEDs, spare I/O headers
Place V_ADC regulator near IMU
  Reduce interference pickup
  Place XBee far away

## Slide 9: Layout, Full Board

## Slide 10: Questions

## Slide 11: Layout, Power Supply
Core Supply
MCU Supply
Fuel Gauge
Charger
Power Switch
JST Connector
Charging LED
Power LED

## Slide 12: Layout, Microcontroller
STM32F4
Microcontroller
8MHz
Oscillator
SPI to
Raspberry PI
To USB
(programming)
I2C to IMU
To Reset Button
UART to XBee
UART to GPS

## Slide 13: Layout, Peripherals
XBee Pro 900
ST 9-DOF IMU Breakout
V_ADC
Supply
Venus GPS Breakout