## Slide 1: ECE 477 Design Review Team 5 Fall 2012
Stephen Carlson
Stephen Ellis
Alec Green
Thor Smith
Thor
Smith
Steven
Ellis
Stephen
Carlson
Alec
Green

## Slide 2: Outline
Project overview
Project-specific success criteria
Block diagram
Component selection rationale
Packaging design
Schematic and theory of operation
PCB layout
Software design/development status
Project completion timeline
Questions / discussion

## Slide 3: Project Overview
We propose an augmented reality simulator
  Allows at least one user to play an electronic game in a mobile, outdoor environment
  Intended for gaming and other simulations that require an augmented environment
Contains two primary parts: a headset and a central control unit (CCU)
  The headset is worn by the user and overlays images of game objects on the user’s view of the environment
  The CCU remains stationary and communicates information to the headset about simulation logic.

## Slide 4: Project Specific Success Criteria
An ability to render graphics based on the orientation of the user’s head.
An ability to render graphics based on the user’s current geospatial location.
An ability to monitor and display the battery power level of the headset to the user.
An ability to monitor and display the status and quality of the wireless connection to the central control unit.
An ability to load headset graphics for a new simulation without re-flashing software on the headset’s microcontroller.

## Slide 5: Block Diagram
Figure 1: The block diagram indicates two functional groups that communicate through the Xbee wireless devices.
The CCU will perform simulation logic
The headset will perform graphics rendering and sensor data acquisition.

## Slide 6: Component Selection Rationale
Headset
  Micro
    GPS and IMU interfacing
    Wireless communication
    Battery monitor interfacing
  Motherboard
    Render graphics
Central control unit motherboard
  Wireless communication
  Data storage
  Game logic

## Slide 7: Microcontroller Constraints
Must be capable of low latency sensor processing
  High speed for floating point math
Required external peripherals
  2 UART (GPS, Wireless module)
  1 SPI (Display/Motherboard connector)
  1 I2C (Power Monitor, IMU)
  At least 10 additional GPIO pins
Prefer 3.3V supply and 3.3V I/O

## Slide 8: Microcontroller Choices
STM32F405RGT6
  ARM-Cortex M4F
  168 MHz with FPU
  192 KB RAM
  64 LQFP 51 I/O
  $11 single quantity
Selected because
  FPU (1 cycle multiply!)
  ART Accelerator (instruction cache)
PIC32MX695F512H
  MIPS
  80 MHz
  128 KB RAM
  64 TQFP 53 I/O
  $10 single quantity
Rejected because
  Lower IPC
  Slower clock

## Slide 9: Motherboard Constraints (CCU)
Uses
  Game logic
  Store game objects to load onto headsets
Required peripherals
  USB for user input device
  1 UART (or USB UART) for Wireless module
  Display output (HDMI, Composite, VGA)

## Slide 10: Motherboard constraints (headset)
Main Constraints
  3D graphics rendering needs fast GPU
Required peripherals
  1 SPI for microcontroller connection
  Display output (HDMI, Composite, VGA)
Other constraints
  Power usage should be suitable for batteries

## Slide 11: Motherboard Choices
Raspberry PI ModelA
  Low-cost ($40 total)
  700 MHz ARM11
  Low-power (2W)
Selected because
  Power consumption
  Community support
  Cost
BeagleBone Black
  $45
  1GHz Cortex-A8
  Low-power (2.5W)
Rejected because
  Slower GPU
  No composite video

## Slide 12: OTHER CHOICES
GPS
  Venus638LPx
    High accuracy (claimed 2.5m) and refresh rate (20Hz)
9DOF
  LSM303DLHC
    Low cost but still high accuracy
    More expensive unit has on-chip filtering but requires NDA
Wireless
  XBee Pro 900HP
    Long range (claimed 6 miles, tested ~300m)

## Slide 13: Packaging Design
Requirements
  Relatively light weight, balanced
  Display focusing and field of view
Materials
  Hat/helmet
  Enclosures for display, PCB/battery stack
  Angle aluminum for mounting frame
  Acrylic or polycarbonate sheet
  Reflective film
  Lenses

## Slide 16: Schematic & Theory of Operation
Accelerometer + Magnetometer (compass) + Gyro determine user orientation
GPS (+ accelerometer) determine geospatial position
All sensor data sent to uC for processing
3.3V: common voltage among all components
168MHz: maximum, performance when processing sensor data, power consumption negligible when compared to other devices

## Slide 17: Schematic (1/2)
Ports A and B to avoid crystal-facing Port C
USART: GPS
USART: Xbee
I2C: Accelerometer + Magnetometer + Gyro
I2C: Battery fuel gauge
SPI: Raspberry Pi
168MHz frequency: maximum, sensor processing performance, negligible power consumption

## Slide 18: Schematic (2/2)
Power
  3.3V .5A Vcore: Raspberry Pi
  3.3V .5A Vmcu: uC + Xbee + GPS
  3.3V .05A Vadc: IMU (low noise)
Ground: ground pour
Bypass caps: manufacturer recommendations
  1x 1uF decoupling on Vbatt
  2x 2.2uF bypass for uC core supply internal regulator
  10x .1uF decoupling power pins
  2x 22uF bulk for regulators

## Slide 19: Schematic (Batt charge + Fuel Gauge)

## Slide 20: Schematic (Power Supplies)

## Slide 21: Schematic (Sensors)

## Slide 22: Schematic (uC)

## Slide 23: PCB Layout – General
Advanced Circuits/4PCB specs
  5mil trace/5mil space
  10mil minimum hole size and 5mil tolerance
For manufacturability
  10mil trace/8mil space
  15mil minimum hole size
No acute angles
Two layers

## Slide 24: PCB Layout – MCU
Oscillator and USB lines match impedance
  Trace lengths must match
  No right angles
Decoupling, oscillator must be adjacent
  Place some capacitors underneath chip
Pin locations determine routing success
0.2mm = about 7 mil difference
(less than one trace width)

## Slide 25: PCB Layout – Power
Total current could be up to 2A
  Use low resistance copper pours
  Multiple large vias for transfer between layers
  Power from multiple directions (“islands”)
  Bulk capacitors near regulator, bypass near loads

## Slide 26: PCB Layout – Other
Connectors
  Raspberry PI connector must match motherboard
  Other connectors must be on edges
Route I2C, UART, SPI lines together
  Test points
Debug LEDs, spare I/O headers
Place V_ADC regulator near IMU
  Reduce interference pickup
  Place XBee far away

## Slide 27: Pcb Layout, Full Board

## Slide 28: Pcb Layout, Power Supply
Core Supply
MCU Supply
Fuel Gauge
Charger
Power Switch
JST Connector
Charging LED
Power LED

## Slide 29: Pcb Layout, Microcontroller
STM32F4
Microcontroller
8MHz
Oscillator
SPI to
Raspberry PI
To USB
(programming)
I2C to IMU
To Reset Button
UART to XBee
UART to GPS

## Slide 30: Pcb Layout, Peripherals
XBee Pro 900
ST 9-DOF IMU Breakout
V_ADC
Supply
Venus GPS Breakout

## Slide 31: Software Design/Development Status
Preliminary drivers to extract GPS and IMU data has been completed. Next steps to push data to GPU and CCU.
The GPU code will be written in OpenGL.
The CCU will provide a user interface and process game logic. C++ for game logic, python for User Interface.
XBee packets flows defined.
GPS Thread
Convert to Decimeters
on x,y
IMU Thread
Convert to pitch, yaw, roll
Control Logic
* Send IMU/GPS over network to CCU/GPU
* Make Decisions based on packets from CCU
XBee Driver
Send/Queue packets.
Connectivity
Battery Thread
Monitor Battery Life

## Slide 32
Team 5 Project Completion Timeline |  |  |  |  | 
 | PCB / Hw | GPU | Data | CCU | Packaging
Week 8 | One to One parts check. PCB Verification |  | Data formats Finalized. |  | Finish Building Headset.
Week 9 | Parts Testing | Prelim Animation | Sensor processing complete. | GUI Software complete | 
Week 10 | Solder Parts to Board Test Power Supply | Animation w/ IMU | Implement network flow. |  | 
Week 11 | Test Micro and other components | Animation w/ GPS | Implement Battery Sensing. | Library for simulations | Evaluation of Headset design
Week 12 |  | Integration w/ Micro |  |  | 
Week 13 |  |  |  | Implement PacMan | Revision of Headset design.
Week 14 |  |  |  |  | 
Week 15 |  |  |  |  | 

## Slide 33: Questions / Discussion