## Slide 1: Team 5 environmental impact analysis
Steven Ellis

## Slide 2: Manufacture (very bad)
Packaging
  Aluminum, ABS, and acrylic
Lithium polymer battery
  LiCoO2 electrode
    LiFePO4 would be less harmful
PCB
  Etching uses either ammonium persulfate
  Lead solder
    Switch to lead-free solder
LCD
  Sulfur hexafluoride used in manufacture
  LED backlighting avoids mercury found in CCFL

## Slide 3: Use (not so bad)
Electricity used to power device
  Only draws ~5 watts in use
  ‘Phantom power’ when turned off is tens of microwatts
Product lifespan
  Battery lasts ~400 charge cycles
    LiFePO4 would increase this to ~2000
  Battery can be replaced without replacing entire unit

## Slide 4: End of life (also pretty bad)
Packaging
  Aluminum and plastics can both be recycled
Lithium polymer battery
  Nonhazardous waste
  Can be recycled
PCB
  Neither biodegradable nor recyclable
LCD
  Neither biodegradable nor recyclable

## Slide 5: Questions?