## Slide 1: Augmented Reality Cornell Cup Mid Review Spring 2014
Stephen Carlson
Steven Ellis
Thor Smith
Thor
Smith
Steven
Ellis
Stephen
Carlson

## Slide 2: Outline
Challenge Definition
Project Entry Solution
Performance Evaluation
Technical Ingenuity
Project Execution Overview
Recommendations and Next Steps

## Slide 3: Outline
Phase 1: Senior Design
  ECE senior design project
Phase 2: Cornell Cup
  Intel/Cornell cup updates

## Slide 4: Challenge Definition
Challenge Definition
Design Requirements
Use Cases

## Slide 5: Challenge Definition
Wearable augmented reality
  Google Glass, Oculus Rift, Epson BT-100
  Promote teamwork
  Substitute for physical objects

## Slide 6: Design Requirements
Portable, comfortable, easy to use
Track position and head orientation
Wireless communication
Maintain real-world perception

## Slide 7: Use Cases
Educational and training
Virtual tour, guide, or navigation
Gaming
  Place “imaginary” objects in real world

## Slide 8: Project Entry Solution
Project Entry Solution
Solution to The Challenge
Block Diagram

## Slide 9: Project Entry Solution
Multi-user gaming
  Multiple games supported
  Integrate with real world
Headset:
  Display
  Orientation tracking
  Location tracking
Backpack:
  Wireless
  Graphics processing
  Simulation logic
  Battery and power

## Slide 10: Solution to The Challenge
Display virtual and real world
  No real-world lag unlike camera
  Interact with real and virtual objects
Track user position and heading
  Update virtual world to match
Communication with other devices

## Slide 11: Block Diagram

## Slide 12: Performance Evaluation
Performance Metrics
  Portability and ease of use
  Position and orientation tracking
  Wireless communication
Performance Results

## Slide 13: Performance Metrics
Portable, comfortable, easy to use
  Mass [kg]
  Total runtime [hours]
  Virtual image quality
  User experience survey

## Slide 14: Performance Metrics
Track position and head orientation
  Location precision [m]
  Head tracking latency [ms]

## Slide 15: Performance Metrics
Wireless communication
  Network refresh [updates per second]
  Wireless range, line of sight [m]
  Simultaneous device limit

## Slide 16: Performance Results
Metric | Phase 1 | Target | Phase 2
Mass [kg] | Headset: 1.3 | Headset: 1 Backpack: 3 | Headset: 1.2 Backpack: 2.5
Total Runtime [hours] | 3 | 3 | 2.5
Location Precision [m] | 1.5 | 2 | 1.5
Wireless Range [m] | 200 | 80 | 110
Display Refresh [FPS] | 10 | 20 | 20
Network Refresh [FPS] | Unimplemented | 20 | 20
Simultaneous Devices | 6 | 16 | 127
Tracking Latency [ms] | 100 | 50 | 50

## Slide 17: Technical Ingenuity
Technical Innovation
Technical Features
  Phase 1
  Phase 2

## Slide 18: Technical Innovation
Overlay virtual world
  Preserve depth perception
  Large field of view (61°)
  Both eyes, reduced eye strain
Head and position tracking
  Digital filtering of orientation
Wireless communication
  Collaborative augmented reality

## Slide 19: Technical Innovation
Self-contained device
  Adjustable for user
  Lightweight, balanced
Functional software
  OpenGL rendering
  Multi-user
  “PacMan” game
  Extensible

## Slide 20: Technical Features (Phase 1)
IMU and GPS interfacing
Long-range 900 MHz wireless
  Requires central server
Efficient power management
  Battery charging

## Slide 21: Technical Features (Phase 2)
High bandwidth Wireless N network
  Up to 127 devices usable at once
  Elimination of dedicated server
Increased virtual image fidelity
  Improved brightness and contrast
  Higher resolution
  Faster graphics engine

## Slide 22: Project Execution Overview
Project Milestones
Challenges
Risk Handling
Budget

## Slide 23: Project Milestones
Phase 1 completion: Dec 2013
  Head tracking and GPS
  Initial software
Cornell Cup Mid Review: Feb 2014
  Increased testing and metrics
  Compare to existing devices
  Improve display visibility

## Slide 24: Project Milestones
Final packaging: Apr 2014
  Final power supply
  Mount new display
Software finalized: Apr 2014
  Multiple headsets networking
  File transfer
  User testing begins

## Slide 25: Challenges
Delays due to coursework, events
DE2i-150 graphics drivers
Power consumption
  Required battery for 3 hours unavailable
User testing

## Slide 26: Risk Handling
Patent liability
  Many existing virtual reality patents
  Licensing may be required
Safety and reliability
  LiFePO4 relatively safe
  Redundant power protection
  Translucent display allows awareness of environment

## Slide 27: Budget
Funding provided by Cornell Cup, Purdue ECE
Major development expenses
  Displays - $205
  Batteries - $114
  Electronics - $130

## Slide 28: Recommendations and Next Steps
Continued software development
  Head tracking and GPS precision
  User interface
Upgrade motherboard
  Longer total runtime, lighter weight
  Better graphics performance
  Significant cost (over $100)

## Slide 29: Recommendations and Next Steps
Alternative input devices
Capitalization
  Software sales, 3rd party development
  Sell to schools for education
  Sell to firms for employee training

## Slide 30: Special Thanks To
Senior Design staff
  Dr. David Meyer, George Hadley, George Toh
The Incredible HUD team
  Aditya B., Blaine Gardner
Dr. Mark Johnson, advisor
Joseph Boettcher, ECE lab staff
Intel and Cornell University

## Slide 31: Questions / Discussion

## Slide 32: PCB Layout, Phase 1

## Slide 33: PCB Layout, Phase 2 Sensor

## Slide 34: PCB Layout, Phase 2 Power

## Slide 35: Schematic, Phase 1

## Slide 36: Schematic, Phase 2 Sensor

## Slide 37: Schematic, Phase 2 Power

## Slide 38: Patents
US 8585476 B2
  Location-based games and augmented reality systems
US 20130267309 A1 [pending]
  Augmented reality and physical games
US 8519844 B2
  Augmented reality and location determination methods and apparatus