## Slide 1: Design Constraint Analysis
Team 05 Augmented Reality Project
TCSP #02
Stephen Carlson, Steven Ellis, Alec Stephen Green, Thor Smith

## Slide 2: Abstract
We propose to build an augmented reality simulator
  Allows at least one user to play an electronic game in a mobile, outdoor environment
  Intended for gaming and other simulations that require an augmented environment
Contains two primary parts: a headset and a central control unit (CCU)
  The headset is portable, worn by the user, and displays images over the user’s view of the environment
    Headsets will overlay game-object pixels displayed by an LED display onto a half-silvered mirror that is suspended in front of the user’s eyes.
  The CCU is not portable. It will communicate information to the headset about simulation logic.

## Slide 3: Functional Block Diagram
Exploring possibility of using another Raspberry PI Model A for rendering

## Slide 4: PSSC Review
An ability to render graphics based on the orientation of the user’s head.
An ability to render graphics based on the user’s current geospatial location.
An ability to monitor and display the battery power level of the headset to the user.
An ability to inform the user of a headset about the status and quality of the wireless connection to the central control unit.
An ability to load graphics for a new simulation to the headset without re-flashing the software on the headset’s microcontroller.

## Slide 5: Controller Requirements
Headset
  Render graphics (PSSC #1, 2)
  GPS (#2) and IMU (#1) interfacing
  Wireless communication (#4)
  Battery monitor (#3) interfacing
Central control unit
  Wireless communication (#4)
  Data storage (#5)

## Slide 6: Microcontroller
Must be capable of rendering graphics
  128 KB or more of RAM
  High speed for floating point math
Required external peripherals
  2 UART (GPS, Wireless module)
  1 SPI (Display/Motherboard connector)
  1 I2C (Power Monitor, IMU)
  At least 10 additional GPIO pins
Prefer 3.3V supply and 3.3V I/O

## Slide 7: Microcontroller
STM32F405RGT6
  ARM-Cortex M4F
  168 MHz with FPU
  192 KB RAM
  64 LQFP 51 I/O
  $11 single quantity
Selected because
  FPU (1 cycle multiply!)
  Large RAM
  Almost all I/O 5VT
PIC32MX695F512H
  PIC 32-bit
  80 MHz
  128 KB RAM
  64 TQFP 53 I/O
  $10 single quantity
Rejected because
  Inefficient architecture
  Slower clock

## Slide 8: Motherboard
Run central control unit (CCU)
  Game logic
  Memory buffer storage for game objects
  Potential future use for complex rendering
    Power usage should be suitable for batteries
Required peripherals
  USB for user input device
  1 UART (or USB UART) for Wireless module
  Display output (HDMI, Composite, VGA)

## Slide 9: Motherboard/Graphics
Raspberry PI Model A
  Low-cost ($40 total)
  700 MHz ARMv6T
  Low-power (2W)
Selected because
  Power consumption
  Cost
Intel Atom/FPGA Board
  Cornell Cup
  Intel Atom processor
  On-board FPGA
Rejected because
  Physical size
  “Over kill”

## Slide 10: Questions
Photo credits:
http://www.sparkfun.com/
http://www.digikey.com/

## Slide 11: Inertial Measurement Unit
ST-EVALMKI108V2
  9 DOF
  Low-cost ($27)
  16-16-12 bit resolution
Selected because
  Low noise density
  High resonant frequency
  Well-documented
MPU-9150
  9 DOF
  Single-chip
  16-16-13 bit resolution
  On-chip DSP
Rejected because
  Cost

## Slide 12: Positioning System
Venus GPS
  20Hz Update
  $60 (incl. antenna)
  External antenna
Selected because
  High resolution
  Good reception quality
GP-635T
  5Hz Update
  $40
  Integrated antenna
Rejected because
  Slow update rate
  Difficult to interface

## Slide 13: Wireless Communication
Digi Xbee Pro
  Self-contained
  No need for smartphone
  Tested 300m range
  $40/unit
Selected because
  Simplicity
  No phone application required
Bluetooth + Cell Radio
  Infrastructure exists
  Unlimited range
  Use 3G/4G/WiFi
  $20/unit + Smartphone
Rejected because
  Reliability
  Latency