## Slide 1: Augmented Reality Cornell Cup Mid Review Spring 2014
Stephen Carlson
Steven Ellis
Thor Smith
Thor
Smith
Steven
Ellis
Stephen
Carlson

## Slide 2: Outline
Challenge Definition
Project Entry Solution
Accomplishments to Date
Technical Ingenuity
Project Execution Overview
Complications
Opportunities
Recommendations and Next Steps

## Slide 3: Challenge Definition
Wearable augmented reality is emerging quickly
  Google Glass, Oculus Rift, Epson BT-100
  Provide information
  Promote teamwork
  Decrease need for physical objects
Design requirements:
  Portable and comfortable
  Track user position and head orientation
  Wireless communication
  Easy to set up and use
  Maintain peripheral vision

## Slide 4: Use cases
Artistic performance
  Performers need to know where to be and when
Train a new employee
  Show a physical demonstration of equipment
  Employee may observe machinery in operation
Educational demonstrations
  Place virtual resources in appropriate locations
Virtual tour, guide, or navigation
Gaming
  Rely on “imaginary” objects placed in a select location
Artistic performance
  Performers need to know where to be and when
Train a new employee
  Show a physical demonstration of equipment
  Employee may observe machinery in operation
Educational demonstrations
  Place virtual resources in appropriate locations
Virtual tour, guide, or navigation
Gaming
  Rely on “imaginary” objects placed in a select location

## Slide 5: Project entry solution
Focus on gaming
Allow for multiple simulations
Multiplayer simulation
Headset:
  Display
  Inertial measurement unit (IMU)
  GPS receiver
Backpack:
  Wireless communication
  Graphics rendering
  Simulation logic

## Slide 7: Accomplishments To Date
Phase 1: Senior Design
Phase 2: Cornell Cup

## Slide 8: Accomplishments To Date (PHA1)
Hardware
  Interfacing to IMU
  Interfacing to GPS
  Power management
    Battery charging
    Battery fuel gauge
    Voltage regulation

## Slide 9: Accomplishments To Date (PHA1)
Self-contained headset
  Adjustable hard hat
  Display mounted to rails
  Electronics in back for balance
Software
  OpenGL ES for 3D rendering
  Networking using XBees
  SPI communication between Raspberry Pi and microcontroller
  PacMan-like game

## Slide 10: Performance metrics
Metric | Phase 1 (Measured) | Phase 2 Target | Phase 2 (Estimate)
Mass | Headset: 1.3kg | Headset: 1 kg Backpack: 3 kg | Headset: ~1kg Backpack: ~2.5kg
Power | ~3 hours | 3 hours runtime | ~4 hours
Location Precision* | ~1.5 m | 2 meters | ~1.5m
Wireless Range | 200 m | 80 m, line of sight | 200 m
Display Refresh | 10 FPS | 20 FPS | 60 FPS
Network Refresh | Unimplemented | 20 FPS | 60 FPS
Usability | Turnkey startup | User can start and use without a technician | Turnkey startup
Simultaneous Device Limit | 5-6 | 16 | 32+
Head Tracking Latency | ~100ms | 50ms* | >=16ms
User survey for subjective measures like comfort, eye strain

## Slide 11: Accomplishments To Date (PHA2)
Power consumption testing
  Provided Terasic board uses 1.2 A typical (14.4 W)
  Acceptable battery life with 60 Wh capacity
Hardware design for Phase 2
  Power supply design
    Battery and regulator selection
  Headset interfacing board
    Re-use GPS, inertial measurement unit,
    microcontroller
Packaging
  Re-use optics
  Selected new display
  Selected helmet and backpack

## Slide 12: Technical Ingenuity
Display virtual environment overlay on real world
  Preserves real-world depth perception
  Large field of view
  Both worlds perceptible simultaneously
  Image perceptible to both eyes
User head and position tracking
  Filtering algorithm for inertial measurement data
Portability and battery operation
Wireless communication to other headsets
  Multi-user augmented reality

## Slide 13: Execution Overview – Timeline 1/3

## Slide 14: Execution Overview – Timeline 2/3

## Slide 15: Execution Overview – Timeline 3/3

## Slide 16: Execution Overview - BUDGET
Name | Vendor | Unit Price | Quantity | Total
Battery | BatterySpace | 66.95 | 2 | 133.90
Screen 1 | Adafruit | 139.95 | 1 | 139.95
Screen 2 | Adafruit | 64.95 | 1 | 64.95
IMU | Mouser | 28.75 | 0 | 0.00
GPS | Sparkfun | 49.99 | 0 | 0.00
Passive Components | Various | 10.00 | 2 | 20.00
Circuit Board (PCB) | OSH Park | 40.00 | 2 | 80.00
Microcontroller | DigiKey | 11.45 | 2 | 22.90
Battery charger | BatterySpace | 39.95 | 2 | 79.90
Voltage regulator | Mouser | 13.23 | 2 | 26.46
Fuel gauge | DigiKey | 6.43 | 2 | 12.86
3D printed box | Purdue IEEE | 40.00 | 2 | 80.00
Backpack | N/A | 10.00 | 0 | 0.00
Development Cost |  |  |  | 739.66

## Slide 17: Complications
Patent Liability
  Many AR patents exist
  Licensing may be required
  Could file new patents and cross-license
User Safety
  LiFePO4 much safer than other Lithium battery chemistries
  Translucent display keeps user aware of environment
  Product unsuitable for use while driving, operating heavy machinery

## Slide 18: Opportunities
Software sales after device purchase
  Create app store
  Encourage third party development
Creation of alternative input devices
  Gloves for tracking hand movement
Business to business sales
  Sell to schools for education
  Sell to businesses for employee training

## Slide 19: Recommendations and Next Steps
Continued software development
  Improve response time of head orientation
  Improve filtering of GPS data (location precision)
    Large “jumps” in position
Migrate software to new motherboard
Finalize packaging modifications for larger display
Testing of new hardware
  Battery power and charging
  Interfacing of Terasic board with existing microcontroller
  Display

## Slide 20: Questions / Discussion

## Slide 22: PCB

## Slide 23: Schematic

## Slide 24: Patents
US 8585476 B2
  Location-based games and augmented reality systems
US 20130267309 A1 [pending]
  Augmented reality and physical games
US 8519844 B2
  Augmented reality and location determination methods and apparatus